## Slide 1
Day 1 IMDRF Industry Joint Workshop | 14 September 2026

## Slide 2: Predetermined Change Control Plan (PCCP) BRAZIL´S PERSPECTIVES
Vivian Morais
Medical Device Pre-market Review Office (GGTPS)
Anvisa - Brazil

## Slide 3: RDC No. 657/2022 is under review
ANVISA Resolution RDC 657/2022, which regulates SaMD in Brazil, is undergoing review four years after its publication to incorporate new regulatory mechanisms and address new technologies—mostly related to AI—from a regulatory standpoint.
One regulatory mechanism being included is the Predetermined Change Control Plan (PCCP), in line with the strategy of continuous harmonization and the adaptation of international mechanisms and regulations to the Brazilian market.

## Slide 4: The new regulatory framework aims to include:
Predetermined Change Control Plan, PCCP;
Two-step approval (innovative software – considering real-world data to progress with approvals);
Specific requirements and principles for AI-powered software (continuous learning AI, protocols, and logic additions);
Harmonized principles for the development of AI software;
Other updates…
Not yet in effect.
Currently undergoing regulatory impact assessment phase.

## Slide 5: PCCP - Harmonizationwith IMDRF (IMDRF/SaMD WG(PD)/N90 DRAFT: 2025)
Requirements are being introduced to facilitate the submission and approval of PCCPs by manufacturers to ANVISA.
The essential principles outlined in IMDRF document N90 were used as the basis for the proposal and were subsequently adapted to the Brazilian regulatory framework.
At this stage, PCCPs will apply only to SaMD. Additional experience and a better understanding of the underlying concepts and their implications are needed before expanding the approach to other types of medical devices.
A dedicated guidance document on PCCPs will be published to provide further details on the requirements and implementation of this framework.

## Slide 6: PCCP - Documentation
The proposal indicates that manufacturers will be required to submit:
- A description of the planned changes to the SaMD;
- A plan for implementing the proposed changes;
- A change protocol describing the methods to be followed for developing, verifying, validating, and implementing the changes, including a performance verification and validation plan, predefined acceptance criteria, a deployment plan, and a user communication strategy;
- An impact assessment, including a risk management analysis outlining the individual and cumulative risks associated with the changes, the corresponding risk mitigation measures, and the anticipated benefits.

## Slide 7: PCCP – New intended use or purpose
PCCP will be not allowed to include new intended use or purpose.
A PCCP should only include changes that remain within the device's originally authorized intended use or intended purpose.
This restriction is imposed in alignment with the agreement reached with the IMDRF and aims to prevent the use of a PCCP to implement fundamental changes to the product.

## Slide 8: PCCP – Changes
Changes to an approved PCCP will be permitted.
A new submission will be required if the modifications:
Significantly affect clinical functionality, safety, or clinical performance;
Alter the SaMD's visual identity;
Change the modifications originally described in the PCCP;
Modify the implementation schedule;
Revise the approved protocols; or
Change the risk management strategy.